NN	2U	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Lodz University of Technology / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 2U / AC voltage controller / Manual version: 6.2 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Control characteristics
### Include your measurement and calculation results together with any formulae used.
The measurements were carried out in the circuit presented in Manual 2U, Sub-chapter 4.1.
Table 1. Measurement and calculation results of power conversion characteristics
∆tα/ms	Pi / W	I / A	Ui / V	Uo / V	α / rad	α / deg	Si/(VA)	Po / W	RLp / Ω	Ir	Por	η	λ

Source (mains) frequency: fs = ? ⇒ mains period Ts = ?
Formulae used for calculations:

### Plot control characteristics of the investigated circuit, i.e. the relative rms output current Ir and the relative average output power Por as functions of the control quantity (thyristor turn-on delay angle α).

Fig. 1. Measured converter control characteristics
### Compare the control characteristics one to another in terms of their linearity: state whether they are close to linear or non-linear, whether this is to the same degree for both quantities and in which section, if applicable.
##### Rms current characteristic:

##### Average power characteristic:

## Load character
### * Based on Table 1, plot the following characteristics of the incandescent lamp used:
#### voltage vs. current (for rms values), U = f(I);
In the investigated circuit, the lamp was the power receiver (load), thus its voltage and current are identical with the converter’s output voltage Uo and output current Io, respectively, while it follows from the converter’s topology that Io = I.

Fig. 2. Voltage vs. current characteristic of the incandescent lamp
#### resistance as a function of rms current, RLp = f(I).

Fig. 3. Incandescent lamp resistance as a function of rms current
### Based on Table 1 (* and on Fig. 3) state in what way the resistance of the incandescent lamp depends on the rms current flowing therein.

### Explain the effect observed referring to the structure of an incandescent lamp as well as to your knowledge about the effect of temperature on resistivity of metals.

### * Do the graphs testify, and in what way they do, to a linear or to a non-linear character of the load in the investigated circuit?

### * Relate the shape of the characteristic of Fig. 2 to the characteristic of Fig. 3.

## Effect of load non-linearity on converter characteristics
### * For a dense set of points in the full control range, α ∊ [0°; 180°], calculate theoretical values of the relative rms current Ir(th) and of the relative average output power Por(th); enter them into the table below.
Table 2. Calculation results of theoretical power conversion characteristics
α / deg	Ir(th)	Por(th)

Formulae used for calculations:

### * Based on data from Table 2, add theoretical curves to Fig. 1 (use solid lines without points).

Fig. 4. Measured and theoretical converter control characteristics
### * In what way do the measured characteristics differ from the theoretical ones? Do these differences change with varying turn-on delay angle α?

### * Justify your observations from point 3.3 referring to results presented in Part 2.

### * Which of the two characteristics has been more heavily affected by load non-linearity?

## Principle of output power control
### Insert the oscilloscope images of the load (lamp) current recorded for two different average output power values.
(a)	(b)

Fig. 5. Load current waveforms at different average output power values: (a) maximum power; b) 50% of maximum power
### In the table below, include:
#### average output power Po and rms load current I as written down during measurements for the two cases as in Fig. 5;
#### load current amplitude Im as read out now from each of the images of Fig. 5 (the Maximum indication).
Table 3. Load current for different average output power values
Po / W	I / A	Im / A

### Check whether the read-out has been correct: for the maximum power case, calculate the rms value I from the value of Im (show the formula used) and compare the result to the value measured for the same case with a meter. If these values are not consistent with each other, determine the source of the discrepancy and correct the erroneous result appropriately.
From the oscilloscope image: I = ?
Comparison conclusion:
### Based on your results in Table 3, analyse current amplitude variations with output power.
#### Is the decrease in the average output power (and thus, of the rms current) accompanied by a change in the amplitude of the current? If so, what is the direction of this change?

#### Justify the above observation referring to results presented in Part 2.

### In what way is the change in rms value I of the load current achieved in the converter investigated so that to decrease the average output power?
#### Quote the defining formula for the rms value I of the load current as a function of its time-varying instantaneous value i(t) (Manual 0, Ref. C).

#### Considering the formula quoted, can the change of the rms value of the current seen in Table 3 be caused by the change of this current’s amplitude seen in the same table? By what principle is this possible or for what reason is it impossible (refer to the formula quoted as well as to the observed fact of increase or decrease of either value)?

#### Apart from the amplitude, what other difference between the waveforms of Fig. 5 can be seen?

#### What is therefore the principle by which the change in the rms value I is introduced? Refer to the defining formula quoted above and analyse the effect of the specific change of the shape of the current waveform seen in Fig. 5 on results of the mathematical operations appearing in that formula.

## Power conversion quality
### Plot characteristics of efficiency η and power factor λ for the investigated circuit as functions of the controlled quantity, i.e. relative average load power Por.
To present the obtained values in the context of the entire possible range of each of them, considering possible measurement errors, an Y-axis range of [0; 1.2] should be applied in both cases.

Fig. 6. Converter efficiency as a function of relative average load power

Fig. 7. Power factor at the converter’s input as a function of relative average load power
### Based on Figs. 6 and 7 justify whether the converter investigated is advantageous (Manual 0, Refs. B and D):
#### for the consumer of electric power?

#### for the owner of the power distribution network?

### How do the analysed parameters change with dimming progress:
#### efficiency?

#### power factor?

### Are the above facts beneficial in view of the circuit’s purpose, i.e. dimming the light at the consumer’s premises?

## Triac application
### Based on the oscilloscope images of the current (Fig. 5), prove that the triac operates as a switch in the circuit investigated (Manual 0, Ref. E).

### Still referring to Fig. 5, classify this switch according to the criterion of controllability (Manual 0, Ref. E).

### Review the selection of the specific triac, BT136‑600E, for the application investigated: compare its ratings (Ref. [12]) to operating conditions, i.e. to values that appear in the real circuit, in the worst case of control (as defined by the turn-on delay angle α):
#### with respect to current:
Measured rms current in the worst case: I = ? at α = ?
Rated rms current: IT(RMS) = ?
The triac has been selected with a margin of: (IT(RMS) − I)/IT(RMS) = ?%
#### with respect to voltage (describe how the value of usw(pk) has been obtained from measurement results):
To identify the worst case and determine the corresponding operating conditions, some knowledge on the investigated circuit’s operating principle will be necessary, especially on the waveform of the switch (triac) voltage usw = uT (vTh in Ref. G). Based on this knowledge, it is possible to relate the unknown value that was not measured to one measured and shown in point 1.1.
Peak voltage in the circuit in the worst case: usw(pk) = ? at α ?
Rated peak voltage: UDRM = ?
The triac has been selected with a margin of: (UDRM − usw(pk))/UDRM = ?%