NN	3P	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Technical University of Lodz / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 3P / Switched-mode operation of power transistors / Manual version: 5.1 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Switching cycle
### In the oscilloscope image (saved in a graphical form) that includes the set of waveforms {uGS; uDS; iD} for a full pulse of the control voltage, mark the different states of the transistor: off-state, turn-on, on-state and turn-off (Manual, Fig. 5 and Ref. C). Insert the image so processed.
For each oscilloscope image that contains more than one waveform, it is obligatory to describe each particular waveform (with its symbol), either directly in the image or in its caption (by referring to numerical designations appearing in the image or to colours provided the report will be delivered in colour).

Fig. 1. Waveforms of uGS, uDS and iD over a full switching cycle with transistor states marked
### In a separate copy of the same original image, mark the steady-state voltage and current levels corresponding to the transistor’s static states: UGS(on), UDS(off), ID(on), UDS(on), as well as the threshold voltage level UGS(th).

Fig. 2. Waveforms of uGS, uDS and iD over a full switching cycle with voltage and current levels in static states as well as the threshold voltage marked
### From the analysed oscilloscope image, read out approximate (with an accuracy of 0.1 div) values of the above-mentioned voltages and currents in static states.
Table 1. Transistor’s voltages and current in static states as measured with an oscilloscope
UGS(on) / V	UDS(off) / V	ID(on) / A	UDS(on) / V

### Justify the values of UGS(on), UDS(off) and ID(on) based on the circuit’s schematic and its component values, including sources, i.e. both power supply voltages (Manual, Sub-chapters 3.1 and 3.3, plus values obtained from the web page). Apply Kirchhoff’s voltage law and Ohm’s law; to simplify, assume that a transistor is an ideal switch (Manual 0, Ref. G).
If it appears that read-outs are inconsistent with what the theory predicts, it is necessary to determine and eliminate the source of any discrepancy before continuing (e.g. incorrect calculations, incorrect read-out or, for current, also unsuitable oscilloscope settings causing incorrect conversion from volts to amps).
UGS(on):
UDS(off):
ID(on):
### * In a separate copy of the same original image mark points, ranges or areas of importance for the assessment of a transistor’s quality as a semiconductor switch, i.e. its proximity to the ideal switch (Manual 0, Ref. G). Include (in the image or below) all the related conditions, i.e. what value each quantity should tend to.

Fig. 3. Waveforms of uGS, uDS and iD over a full switching cycle together with parameters important for a transistor’s application as a switch

## Drain-source resistance and threshold voltage
### Include measurement results of the RDS resistance obtained with a multimeter, assigning each of them to an appropriate case as indicated in the first column: on-state resistance RDS(on), off-state resistance RDS(off) or threshold voltage UGS(th) (i.e. the measurement for which a drastic drop in resistance was observed).
Table 2. Drain-source resistance and threshold voltage measurement results
	Multimeter		* Oscilloscope		Data sheet
Case	UGS / V	RDS	UGS / V	RDS	UGS / V	RDS
RDS(off)	0		×	×	0
UGS(th)				×		×
RDS(on)

### Calculate the mutual ratio of the off-state to the on-state resistance. How many orders of magnitude is this?
RDS(off) / RDS(on) = ?
### Add data sheet-based values for the transistor investigated to Table 2.
#### Calculate the off-state resistance RDS(off) corresponding to the leakage current given in the data sheet of the investigated transistor IDSS, for a temperature consistent with laboratory measurement conditions (i.e. room temperature). Apply Ohm’s law together with the IDSS measurement condition indicated in the data sheet. Based on the character of the IDSS value indicated in the data sheet (minimum, typical or maximum), determine the resulting character of the result obtained; add an appropriate subscript to the resistance symbol below and prefix the value in the table with the symbol ≥, ≈ or ≤, as appropriate.
RDS(off) = ?
#### Directly copy values for the threshold voltage UGS(th) and the on-state resistance RDS(on) along with a corresponding UGS value.
### Compare (formulate a sentence describing a relationship) both the above drain-source resistance values as measured with a multimeter to the respective data sheet-based values. Justify possible discrepancies considering measurement conditions and value spread for data sheet parameters (minimum / typical / maximum) and the multimeter’s measurement uncertainty.
The measurement uncertainty with the multimeter used is ±0.06 Ω for its lowest resistance range and ±1% for its 5 MΩ range.

### * Calculate the value of RDS(on) from the appropriate oscilloscope measurement results (Table 1). Add the result to Table 2. Compare it (formulate a sentence describing a relationship) to the multimeter measurement result and to the value provided in the data sheet; justify possible discrepancies.
For the ranges used, the measurement uncertainty with the oscilloscope used is 3% of value + 0.1 div for any voltage (including one coming from the current probe) . The measurement uncertainty of resistance as a quotient of two values will be greater, in accordance with metrology rules.
RDS(on) = ?

### Compare (formulate a sentence describing a relationship) the threshold voltage value UGS(th) obtained by the measurement of the RDS resistance with a multimeter (Table 2) to the one given in the data sheet.

### * From the oscilloscope image presented in Fig. 2, read out the value of the threshold voltage UGS(th) and add it to Table 2. Compare it (formulate a sentence describing a relationship) to the multimeter measurement result and to the value provided in the data sheet.

## Transistor as a switch in static states
### Assess the effect of the transistor as a closed switch on the power loop of the investigated circuit:
#### compare (formulate a sentence describing a relationship) the on-state drain-source resistance to the load resistance RL; how many orders of magnitude is this difference?

#### applying the Kirchhoff’s voltage law, calculate the transistor’s on-state principal current ID(on), similar to point 1.4 (use the same value for the supply voltage UDD), but considering the non-zero RDS resistance (Table 2) this time;

#### compare the result obtained now with the one got in point 1.4 (when an ideal switch was assumed), expressing the difference as a percentage;
|ID(on)id − ID(on)|/ID(on) = ?
#### when in its on-state, does the transistor have a significant impact on the value of current in the power loop? hence, was the simplifying assumption of point 1.4 reasonable?
In this context, an effect of 1% should be considered insignificant, while one of 10%, significant.

### Assess the effect of the transistor as an open switch on the power loop of the investigated circuit:
#### compare (formulate a sentence describing a relationship) the off-state drain-source resistance to the load resistance RL; how many orders of magnitude is this difference?

#### applying the Kirchhoff’s voltage law, calculate the transistor’s off-state principal voltage UDS(off), similar to point 1.4 (use the same value for the supply voltage UDD), but considering the finite RDS resistance (Table 2) this time;

#### compare the result obtained now with the one got in point 1.4 (when an ideal switch was assumed), expressing the difference as a percentage;
|UDS(off)id − UDS(off)|/UDS(off) = ?
#### when in its off-state, does the transistor have a significant impact on the distribution of voltages in the power loop? hence, was the simplifying assumption of point 1.4 reasonable?

### When does the transistor’s non-ideality affect the power loop to a greater extent: in its on-state or in its off-state?

### Based on your answers from points 3.1 and 3.2 justify whether the transistor has been properly selected for switched-mode operation in the investigated circuit (Manual 0, Ref. G).

### Using measurement results of resistance (Table 2) and current or voltage, as appropriate (Table 1), apply the Joule’s law in a suitable form to calculate the instantaneous drain power loss in the transistor in its either static state (Ref. A for the conducting state).
##### Conducting (on) state:
pD(cond) = ?
##### Blocking (off) state:
pD(b) = ?
### Compare (formulate a sentence describing a relationship) the two results one to another (how many orders of magnitude is the difference?) and judge whether they justify the assumption applied in practice that the off-state is negligible in respect of power loss?

## Operation in dynamic states
### In the oscilloscope image (saved in a graphical form) of the waveform set {uGS; uDS; iD} for the transistor’s turn-on and turn-off, mark time intervals where the transistor operates in each of its modes: sub-threshold, saturation or linear (Manual, Fig. 5).
The directive of 1.1 still applies.

(a)

(b)
Fig. 4. Waveforms of uGS, uDS and iD with the transistor’s operating modes marked: (a) turn-on; (b) turn-off
### * Based on the waveform of the uGS voltage during turn-on, demonstrate that the input capacitance Cin varies in the course of this process (Refs. B and C). Indicate the time interval where the Miller’s effect can be observed.

### * Insert the oscilloscope image of the voltage set {uGS, uDS} recorded at a zero supply voltage UDD.
The directive of 1.1 still applies.

Fig. 5. Waveforms of uGS and uDS at UDD = 0
### * What is the difference between the uGS waveforms of Fig. 4a and of Fig. 5? Explain this difference by referring to the Miller’s effect (Ref. B) and to the respective waveforms of the uDS voltage.

## Operating point trajectory
### Include your calculations of load line parameters for a resistive load.
U0 = ?
I0 = ?
### Insert the plots of the transistor’s operating point trajectory obtained in the Octave package with the transistor’s static characteristics in the background, together with the load line added for an ideal resistive load, with operating regions labelled, as well as of the plots of power loss corresponding to this trajectory.

(a)

(b)
Fig. 6. Operating point trajectory for the transistor with its output characteristics in the background, together with with the ideal resistive load line (top plot) and the corresponding transistor’s principal circuit power loss (bottom plot): (a) turn-on; (b) turn-off
### Do the extreme points of the recorded trajectory for either static state conform to expectations (formulate these expectations)?
##### Off-state

##### On-state

### What load character do the plotted operating point trajectories indicate (Ref. D; Manual 0, Ref. G)? Does this load appear to be an ideal or as a real (practical) one?

### By analysing the operating point trajectory plots as juxtaposed with the corresponding power loss plots, determine where in the output characteristic plane the greatest power losses occur and where, the lowest ones. Which operating modes of the transistor do these loci correspond to?

### Considering your answer from point 5.5, in which operating modes may a transistor operate continuously and in which, it should work for the shortest time possible if heat dissipation in this device is to be minimised?