NN	3U	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Technical University of Lodz / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 3U / Buck DC Converter / Manual version: 7.2 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Semiconductor switch
### Include oscilloscope images of the inductor current iL, the transistor current iT, the diode current iD along with the transistor control voltage ug.
For each oscilloscope image that contains more than one waveform, it is obligatory to describe each particular waveform (with its symbol), either directly in the image or in its caption (by referring to numerical designations appearing in the image or to their vertical order).
(a)

(b)

(c)

Fig. 1. Current waveforms in the buck converter circuit along with the transistor control voltage ug: (a) inductor current iL; (b) transistor current iT; (c) diode current iD
### Based on Fig. 1, determine the relation between the control voltage ug supplied to the gate of the transistor and the state of this device (on/​off). Point out specific features of an appropriate waveform that indicate the state of the transistor.

### Based on Fig. 1 demonstrate that in the investigated circuit, the MOSFET and the diode form a single-pole double-throw switch (Ref. C)
Whenever manual or reference is mentioned in this report template, this refers to Manual 7K unless stated otherwise.

## Circuit component roles
### Include waveform sets {ug, iL} and {ug, uo} recorded for three configurations of the circuit: (1) with passive components absent (at the output); (2) with just the inductor present; and (3) with both the inductor and the (output) capacitor present.
Oscilloscope images of {ug, iL} and {ug, uo} for a given configuration should be placed next to each other, on the left and on the right, respectively. The directive of point 1.1 still applies.
(a)

(b)

(c)

Fig. 2. Waveforms of ug and iL (left) as well as of ug and uo (right), in the circuit: (a) with passive components absent at the output; (b) with the inductor present; (c) with the inductor and the output capacitor present
### By comparing subsequent oscilloscope images of Fig. 2, determine the effect of the insertion of the particular components (Manual, Sub-chapter 5.2):
Each of the components listed fulfils just one task. Therefore in each case, such a feature of the waveforms should be determined that was clearly introduced by the given component while it was not introduced by any other one, i.e. a feature that was not observed before the considered component was inserted and that did not change after the subsequent component was inserted.
#### the semiconductor switch;
This configuration should be compared against a circuit where, instead of the switch, a permanent connection would exist between the converter’s input and output.

#### the inductor;
In this case, due to the output capacitor being absent, the inductor current iL is identical with the output current io. The output voltage uo is therefore strictly coupled with the inductor current through the Ohm’s law as applied to the load RL. Inserting the inductor has a primary effect on just one of these waveforms while any change in the other one is just a derived consequence, only resulting from the existence of the above coupling.

#### the (output) capacitor.

### * Based on known circuit component values (ultimate results of component selection from Exercise 7K) and circuit operating conditions, i.e. load and control (design requirements), determine whether conditions are met that are necessary for the inductor and the output capacitor to correctly fulfil their roles (Manual, Sub-chapter 5.1). Include suitable calculations for conditions corresponding to Fig. 2, i.e. the nominal ones.

### * Justify whether the waveforms of Fig. 2 confirm that the above-mentioned theoretical conditions are indeed the conditions for a correct operation of the inductor and the capacitor.

## Operating parameters under nominal conditions
### Include oscilloscope images of inductor current and output voltage recorded under nominal operating conditions of the complete converter (Ui, Uo).

Fig. 3. Waveforms of ug and iL (left) as well as of ug and uo (right) in the circuit with the inductor and the output capacitor present, operating under nominal conditions
### From the oscilloscope image of Fig. 3, obtained for the complete converter circuit (i.e. with the inductor and the output capacitor present), read out the values of: the output voltage Uo, the direct component of the inductor current IL(0) and the ripple amplitude of the inductor current ∆iL.
Table 1. Output voltage and inductor current
Uo / V	IL(0) / A	∆iL / A

### Justify the above values by referring to known circuit component values and circuit operating conditions, i.e. supply, load and control. Include suitable calculations (Ref. B).
##### Circuit components
According to ultimate component selection results from Exercise 7K:
L1 = ?
C5 = ?
##### Supply and load conditions
Nominal value according to design requirements:
Ui ≈ ?
Value calculated for nominal operating conditions and used over this exercise:
RL = ?
##### Control conditions
Value measured in Exercise 7K for nominal conditions:
fs = ?
Value set and shown in Fig. 3:
D = ?
##### Justification of operating parameters measured
Uo ≈ ?
IL(0) ≈ ?
∆iL ≈ ?
## Efficiency
### Include measurement and calculation results of the converter’s characteristics as functions of the duty cycle.
Table 2. Measurement results of electrical quantities at the converter’s input and output as functions of transistor current duty cycle
DiT	Ui / V	Ii / A	Uo / V	Io / A

Table 3. Calculation results of the converter’s parameters as functions of transistor current duty cycle
DiT	Pi / W	Po / W	η	KU	KU(id)	KU/KU(id)	* KI

### Based on data from Table 3, plot a characteristic of efficiency η as a function of transistor current duty cycle DiT. To make an analysis of this characteristic’s shape and location easier, make the range of either axis identical with the theoretically possible range of the corresponding parameter (D or η as appropriate).

Fig. 4. Efficiency characteristic as a function of transistor current duty cycle
### Based on Fig. 4 determine whether the level of efficiency obtained is high or low as compared to linear-mode circuits (Manual 0, Ref. E).

### Does efficiency vary with the transistor current duty cycle in the investigated range? If so, then in what way and how strong is this variation?

### Compare the value of efficiency as measured on the real circuit against:
#### its value initially assumed in design (Exercise 7K, Task 1);

#### its value estimated based on transistor power loss estimation (Exercise 7K, Task 4).

### What can be some specific sources of the discrepancy noticed above between the estimated and the measured values, considering the estimation methodology applied and related simplifications (Exercise 7K, Task 4)?

## Voltage conversion ratio
### Include a table showing values of voltage conversion ratio for an ideal converter over a dense set of duty cycle values.
In an ideal circuit, i.e. one where the switch is ideal, switching would be immediate and infinitesimally short. Thus in this case, the duty cycle of the transistor current DiT is identical with the duty cycle of the control waveform D.
Table 4. Voltage conversion ratio of an ideal converter as a function of transistor current duty cycle
DiT	KU(id)

### Based on Table 3, plot the following as functions of transistor current duty cycle DiT:
#### voltage conversion ratios: measured for the real converter KU as well as calculated for an ideal converter KU(id) (the latter exceptionally based on Table 4, so that the characteristic for an ideal circuit looks as a smooth curve and that it covers the full theoretically possible range of duty cycle);

Fig. 5. Voltage conversion characteristics for the real and an ideal circuit as functions of transistor current duty cycle
#### the mutual ratio of voltage conversion ratios, real circuit to ideal circuit, i.e. the quotient of KU/KU(id), along with real circuit efficiency η, applying axis ranges as in Fig. 4.

Fig. 6. Mutual ratio of voltage conversion ratios (real circuit to ideal circuit) and real circuit efficiency as functions of transistor current duty cycle
### What is the direction (is the real circuit value greater or lower than the ideal circuit one?) of discrepancy in voltage conversion rate between the real circuit and an ideal circuit?

### Based on Fig. 6 determine whether the expected relationship exists between the real and ideal circuit voltage conversion rates and the efficiency of the former (Manual, Sub-chapter 5.5). Quote this relationship.

### Considering your answer from point 5.4, what is the primary source of the discrepancy noticed in point 5.3?

### Quote and compare in words two duty cycle values for nominal conditions: the one predicted during design and the one ultimately set to obtain the required value of the output voltage.
Duty cycle predicted during design based on estimated efficiency (Exercise 7K, Task 4):
Dnom(est) = ?
Duty cycle that had to be set to obtain the output voltage required in design (Fig. 2):
Dnom(set) = ?

### Explain the discrepancy observed referring to your answers from points 5.3-5.5 and 4.5-4.6.

## Input current
### Based on Table 2, determine whether the input current Ii varies with a decreasing input voltage Ui. What is the direction of this variation?

### Explain why the input voltage varied despite the load (output current Io) being held constant (Manual, Sub-chapter 5.5).

### * Include a table showing theoretical values of the current conversion ratio for a dense set of duty cycle values.
Table 5. Theoretical current conversion ratio as function of transistor current duty cycle
DiT	KI(teor)

### * Based on Tables 3 and 5, plot measured and theoretical values of the current conversion ratio KI as a function of transistor current duty cycle.

Fig. 7. Measured and theoretical current conversion ratio as a function of transistor current duty cycle

### * Based on Fig. 7, determine if the expected relationship exists between the direct component of the input current and the output current (Manual, Sub-chapter 5.4).

### * According to Fig. 7, do power losses affect the above-mentioned relationship in the real converter (Manual, Sub-chapter 5.5)?

## Transistor power loss minimisation
### Assume that you aim at increasing the converter’s efficiency by reducing transistor static and dynamic power loss, PT,stat and PT,dyn, by a factor of at least two. According to what criteria would you search for a suitable transistor? Justify your answer by quoting appropriate formulae applied to perform calculations in Exercise 7K. Express these criteria with numbers in the form of inequalities, based on the data sheet of the specific transistor applied in your assembled converter.

### * Should the replacement of the transistor not be an option due to cost considerations, what other step could be taken to influence its operation so that the converter’s efficiency increases? Base on conclusions formulated in your report on Exercise 4P.

### * What additional modification of the converter circuit would be necessary so that the change indicated above could be introduced? Look for the answer in your design calculations performed in Exercise 7K and related to the relevant circuit component.