NN	4P	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Lodz University of Technology / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 4P / Dynamic Properties of Field-Effect Transistors / Manual version: 6.1 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Parameters of static states
### Insert oscilloscope images (ones saved in a graphical form) containing the sets of waveforms {uGS; uDS; iD} and {uGE; uCE; iC}, respectively, for a full control voltage pulse.
For each oscilloscope image that contains more than one waveform, it is obligatory to describe each particular waveform (with its symbol), either directly in the image or in its caption (by referring to number/letter designations appearing in the image or to colours provided the report will be delivered in colour).

(a)

(b)
Fig. 1. Voltage and current waveforms for the investigated transistors over a full switching cycle: (a) uGS, uDS, iD for the MOSFET; (b) uGE, uCE, iC for the IGBT
### From the oscilloscope images inserted, read out approximate (with an accuracy of 0.1 div) values of voltages and currents in static states, as specified in the table below.
Table 1. Transistor voltage and current values in static states
MOSFET
UGS(on) / V	UDS(off) / V	ID(on) / A

IGBT
UGE(on) / V	UCE(off) / V	IC(on) / A

### Justify the above values based on the circuit’s schematic and its component values, including sources, i.e. both power supply voltages (Manual, Sub-chapters 3.1 and 3.2, plus values obtained from the web page). Apply Kirchhoff’s voltage law and Ohm’s law; to simplify, assume that a transistor is an ideal switch (Manual 0, Ref. G).
As the same measurement circuit was used for both transistors, set-up in exactly the same way, corresponding values for both devices should be equal one to another.
If it appears that read-outs are inconsistent with what the theory predicts, it is necessary to determine and eliminate the source of any discrepancy before continuing (e.g. incorrect calculations, incorrect read-out or, for current, also unsuitable oscilloscope settings causing incorrect conversion from volts to amps).
UGS(on) ≈ UGE(on):
UDS(off) ≈ UCE(off):
ID(on) ≈ IC(on):
## Time-related parameters for the MOSFET
### Include the dynamic parameter values determined for the MOSFET.
Table 2. Dynamic parameters of the turn-on state for the MOSFET, for different gate resistances
RG / Ω	td(on) / ?	tr / ?	PD(on)pk / ?	WD(on) / ?

Rate of Decrease, qdecr(LH)

Table 3. Dynamic parameters of the turn-off state for the MOSFET, for different gate resistances
RG / Ω	td(off) / ?	t‌f / ?	PD(off)pk / ?	WD(off) / ?

Rate of Decrease, qdecr(LH)

### Include the calculated powers of the rate of decrease of the gate resistance qdecr(LH)(RG).
Table 4. Subsequent powers of the rate of decrease of the gate resistance
α	0	0.5	1	1.5	2
[qdecr(LH)(RG)]α

### Based on Tables 2 and 3, determine the effect of the gate resistance RG on the time-related parameters of the transistor: td(on) and tr as well as td(off) and t‌f. Describe each effect both qualitatively (a value increased / decreased / stayed constant) and quantitatively (e.g. insignificantly, proportionally, clearly stronger or weaker). To assess results quantitatively, compare the quotient qdecr(LH) calculated for a given parameter to the quotient for the gate resistance RG, making use of Table 4.
If the quotient qdecr(LH) for a given parameter is equal to the quotient for the gate resistance RG raised to a power of α = 1 (according to Table 4), then this means that this parameter is proportional to RG; if to a power of α = 2, then this parameter is proportional to the square of RG;; if to a power of α = 0, then it is independent of RG; if to a power of α < 0, then it is accordingly inversely proportional.
The value of qdecr(LH) raised to the power of α = 0.5 determines the limit below which a given parameter can be considered fairly independent of RG (more or less approximately, depending on the distance from the power of α = 0); and above which this parameter can be considered approximately proportional to RG (more or less approximately, depending on the distance from the power of α = 1). By analogy, the value of qdecr(LH) raised to the power of α = 1.5 determines the limit between a relationship of approximate proportionality to RG and one of approximate proportionality to RG2.

### Explain the above observations by referring to the field-effect transistor input circuit model in the form of an input capacitance (Manual 3P, Ref. C).

### * Quote time-related parameter values provided in the data sheet. Do the values obtained by measurement are in accordance (as to the order of magnitude) with the data sheet ones? Explain possible discrepancies noting the issue of measurement conditions.
Table 5. Nominal values of time-related parameters of the MOSFET according to its data sheet
Parameter	Value	Unit
td(on)
tr
td(off)
t‌f

## Energy-related parameters of the MOSFET
### Based on Tables 2 and 3, determine the effect of the gate resistance RG on the energy dissipated during turn-on WD(on) and (separately) on the energy dissipated during turn-off WD(off). Describe each effect both qualitatively (a value increased / decreased / stayed constant) and quantitatively (e.g. insignificantly, proportionally, clearly stronger or weaker). To assess results quantitatively, compare the quotient qdecr(LH) calculated for a given parameter to the quotient for the gate resistance RG, making use of Table 4.
##### Energy dissipated during turn-on:

##### Energy dissipated during turn-off:

### In the same manner, determine the effect of the gate resistance RG on the peak power loss during turn-on PD(on)pk and during turn-off PD(off)pk.
##### Peak power loss during turn-on:

##### Peak power loss during turn-off:

### Justify your qualitative and quantitative observations from point 3.1 based on the most generic formula relating energy to power (Manual 6P, Sub-Chapter 2.2; quote this formula). Make use of your observations regarding peak power loss (point 3.2; as the waveform shape does not change from case to case, the peak value is a good descriptor of the entire waveform) and those regarding time-related parameters (point 2.3).

### Based on data from Tables 2 and 3, for either gate resistance value, calculate and include in the table below:
#### the total switching time tsw(tot), as the sum of all the times td(on), tr, td(off) and tf;
#### the average dynamic power loss PD(dyn) in the transistor investigated for an example frequency of fs = 100 kHz, as an appropriate function of the dissipated energy [Manual 3P, Ref. C, formula (10.59) with its right-hand side reduced to its one respective component].
Table 6. Total switching time and average dynamic power loss in the MOSFET, for different gate resistances
RG / Ω	tsw(tot) / ?	PD(dyn) / ?

Formula used:
Pd(dyn) =
### Based on your results included in Table 6, justify which power semiconductor devices are more advantageous from the point of view of dynamic power loss in a switch (Manual 0, Ref. G): ones with short or ones with long switching times.

## Time-related parameters for the IGBT
### Include the dynamic parameter values determined for the IGBT.
Table 7. Dynamic parameters of the turn-off state for the IGBT, for different gate resistances
RG / Ω	td(on) / ?	tr / ?	WC(on) / ?

Rate of Decrease, qdecr(LH)

Table 8. Dynamic parameters of the turn-off state for the IGBT, for different gate resistances
RG / Ω	td(off) / ?	t‌f / ?	WC(off) / ?	WC(off,z) / ?	t‌int(off) / ?	Iz / ?	tz(phys) / ?

Rate of Decrease, qdecr(LH)

### Based on Tables 7 and 8, determine the effect of the gate resistance RG on each (i.e. each one separately) time-related parameter of the transistor: td(on) and tr as well as td(off) and t‌f. Describe each effect both qualitatively (a value increased / decreased / stayed constant) and quantitatively (e.g. insignificantly, proportionally, clearly stronger or weaker). To assess results quantitatively, compare the quotient qdecr(LH) calculated for a given parameter to the quotient for the gate resistance RG, making use of Table 4.
##### Turn-on delay time:

##### Rise time:

##### Turn-off delay time:

##### Fall time:

### * Analyse the usefulness of various time-related turn-off parameters:
#### what percentage of the integration interval t‌int(off) (corresponding to the energy dissipated during turn-off WC(off)) is the fall time tf?
tf / t‌int(off) = ?

#### if the above times are referenced to the waveforms recorded (Fig. 7), which one does reflect the duration of transient processes during turn-off?

#### does the turn-off time toff describe well the turn-off process of an IGBT (justify)?

#### what percentage of the integration interval t‌int(off) is the tail time tz(phys)? is the latter significant or negligible in this context?
tz(phys) / t‌int(off) = ?

## Current tail
### Based on Table 8 assess how significant the effect of the gate resistance on the current tail’s magnitude and duration has been.
A change less than 10% should be considered insignificant as well as doubtful due to the limited measurement accuracy (including the determination of the t7 coordinate).

### Explain the above observations by referring to physical operation bases of the IGBT (Ref. B). What parameters do therefore the current tail magnitude and duration depend on?

### * For an arbitrarily chosen value of RG, calculate the ratio of current tail magnitude Iz (Table 8) to the total on-state collector current IC(on) (Table 1).
Iz / IC(on) = ?
### * Using the result obtained, calculate the current gain of the PNP component of the IGBT and the MOS channel current of the same in the case analysed.
αpnp = ?
Imos = ?
## Energy-related parameters of the IGBT
### Based on Tables 7 and 8, determine the effect of the gate resistance RG on the energy dissipated during turn-on WC(on) and (separately) on the energy dissipated during turn-off WC(off). Describe each effect both qualitatively (a value increased / decreased / stayed constant) and quantitatively (e.g. insignificantly, proportionally, clearly stronger or weaker). To assess results quantitatively, compare the quotient qdecr(LH) calculated for a given parameter to the quotient for the gate resistance RG, making use of Table 4.
##### Energy dissipation during turn-on:

##### Energy dissipation during turn-off:

### What percentage of the turn-off energy WC(off) is related to the current tail (WC(off,z))? Is this contribution significant or negligible?
Wc(off,z) / WC(off) = ?

### Describe the effect of the gate resistance RG on the energy dissipation component related to the current tail WC(off,z).
The remark of point 5.1 still applies.

### Explain the above observation based on the generic formula relating energy to power (by analogy to point 3.3) and your answer from point 5.1.

### Explain your qualitative observations made in point 6.1:
#### in respect of the turn-on energy WC(on), based on the formula relating energy to power and your answer from point 4.2 (you can also use your answer from point 3.3);

#### in respect of the turn-off energy WC(off), based on your answers from points 6.2 and 6.3.

## IGBT compared to MOSFET
### Indicate similarities and differences between the MOSFET and the IGBT in respect of waveform shapes (Figs. 2, 3, 6 and 7) in the turn-on state and in the turn-off state.
##### Turn-on state:

##### Turn-off state:

### Using your observations and conclusions formulated in Parts 2 to 6, determine how the differences stated above will translate into differences between the MOSFET and the IGBT in time-related and in energy-related parameters.
As it was a specific MOSFET and a specific IGBT that were investigated, values from Tables 2 and 3 should not be compared to those from Table 7 and 8, as numerical data obtained for two selected items cannot form a basis for conclusions on general regularities applicable to all transistors. However, you can refer to observations and conclusions formulated on their basis, as they referred to relationships between parameters and not to values of these parameters as such.

### By comparing your answers in points 4.2 and 6.1 to your answers in points 2.3 and 3.1 state whether the control circuit affects each of the particular dynamic parameters (both time-related and energy-related) of the IGBT to the same extent as it affects the respective parameters of the MOSFET. For which parameters is this effect clearly weaker?

### In what way does the weaker effect stated above follow from the difference in physical operation bases of the considered transistors? Why does it only concern the specific parameters listed above and not other ones (Ref. B)?

### Considering the full answer (i.e. together with its justification) from point 3.5 and referring to your answers in points 7.2 and 7.4, assess which of the two transistor types analysed exhibits more advantageous dynamic properties.

## Check plots for dynamic parameters
##### MOSFET, gate resistance RG ≈ 470 Ω

(a)

(b)

(c)
Fig. 2. Check plots illustrating the determined turn-on dynamic parameters of the MOSFET, for RG ≈ 470 Ω: (a) td(on); (b) tr; (c) WD(on)

(a)

(b)

(c)
Fig. 3. Check plots illustrating the determined turn-off dynamic parameters of the MOSFET, for RG ≈ 470 Ω: (a) td(off); (b) tf; (c) WD(off)
##### MOSFET, gate resistance RG ≈ 220 Ω

(a)

(b)

(c)
Fig. 4. Check plots illustrating the determined turn-on dynamic parameters of the MOSFET, for RG ≈ 220 Ω: (a) td(on); (b) tr; (c) WD(on)

(a)

(b)

(c)
Fig. 5. Check plots illustrating the determined turn-off dynamic parameters of the MOSFET, for RG ≈ 220 Ω: (a) td(off); (b) tf; (c) WD(off)
##### IGBT, gate resistance RG ≈ 470 Ω

(a)

(b)

(c)
Fig. 6. Check plots illustrating the determined turn-on dynamic parameters of the IGBT, for RG ≈ 470 Ω: (a) td(on); (b) tr; (c) WC(on)

(a)

(b)

(c)

(d)
Fig. 7. Check plots illustrating the determined turn-off dynamic parameters of the IGBT, for RG ≈ 470 Ω: (a) td(off); (b) tf; (c) WC(off); (d) WC(off,z)
##### IGBT, gate resistance RG ≈ 220 Ω

(a)

(b)

(c)
Fig. 8. Check plots illustrating the determined turn-on dynamic parameters of the IGBT, for RG ≈ 220 Ω: (a) td(on); (b) tr; (c) WC(on)

(a)

(b)

(c)

(d)
Fig. 9. Check plots illustrating the determined turn-off dynamic parameters of the IGBT, for RG ≈ 220 Ω: (a) td(off); (b) tf; (c) WC(off); (d) WC(off,z)