NN	5P	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Lodz University of Technology / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 5P / Static properies of power transistors / Manual version: 5.9 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Static forward characteristics
### Insert curve tracer images showing static forward output characteristics of the transistors investigated with visible operating regions marked and labelled.

(a)

* (b)

(c)

(d)
Fig. 1. Static forward output characteristics of the transistors investigated with operating regions marked: (a) BJT (single); (b) Darlington BJT; (c) MOSFET; (d) IGBT
### Include numerical data that describe the conducting state of each transistor as functions of its principal current, as appropriate: read out from an output characteristic (together with images showing measurement point locations), read out from a data sheet or calculated (provide any formulae used).
To calculate Ploss and Pctrl, a duty cycle D = ? has been assumed; additionally, to calculate Pctrl for field-effect transistors, a switching frequency fs = ? has been assumed.
The values of Io and Uon as well as IB, UGS and UGE have been read out from Figs. 2 to 5. The values of UBE(sat) and QG(on) have been read out from data sheets. The remaining quantities have been calculated using the formulae:
?
##### BJT (single)

Fig. 2. Static forward output characteristic of the BJT investigated with measurement points and base current values marked
Table 1. Conducting state parameters read out and calculated for the BJT as functions of its principal current
Io / ?	Uon / ?	IB / ?	UBE(sat) / ?	Ron / ?	Ploss / ?	Pctrl / ?

##### Darlington BJT

Fig. 3. Static forward output characteristic of the Darlington BJT investigated with measurement points and base current values marked
Table 2. Conducting state parameters read out and calculated for the Darlington BJT as functions of its principal current
Io / ?	Uon / ?	IB / ?	UBE(sat) / ?	Ron / ?	Ploss / ?	Pctrl / ?

##### MOSFET

Fig. 4. Static forward output characteristic of the MOSFET investigated with measurement points and gate-source voltage values marked
Table 3. Conducting state parameters read out and calculated for the MOSFET as functions of its principal current
Io / ?	Uon / ?	UGS / ?	QG / ?	Ron / ?	Ploss / ?	Pctrl / ?

##### IGBT

Fig. 5. Static forward output characteristic of the IGBT investigated with measurement points and gate-emitter voltage values marked
Table 4. Conducting state parameters read out and calculated for the IGBT as functions of its principal current
Io / ?	Uon / ?	UGE / ?	QG / ?	Ron / ?	Ploss / ?	Pctrl / ?

## On-state voltage drop and resistance
### Based on Tables 1 to 4, create plots showing the following as functions of the principal current Io [all the three (* four) devices in a single plot for each physical quantity listed]:
#### the on-state voltage Uon, however, with axes swapped so that to obtain a coordinate system as in traditional presentations of forward characteristics (X-axis for voltage, Y-axis for current), using the linear scale for both axes, with the system’s origin at (0; 0);
The final fragment of the above instruction does not mean that a point of (0; 0) should be added to measurement data as such a point was not read out; it does not mean either that approximated transistor characteristics should be drawn down to this point as this would require reading out much more points in the neighbouring range.

Fig. 6. On-state voltage as a function of principal current
#### on-state resistance Ron, applying the logarithmic scale for both axes to make determining the relationship nature easier.
A quantity b as a function of another quantity a is presented in such a manner that the X-axis corresponds to the quantity a, while the Y-axis, to the quantity b.

Fig. 7. On-state resistance as a function of principal current
### Determine the nature and the strength of the relationships observed, dividing the devices investigated into two groups (Manual 0, Ref. H; Manual 1, Refs. A and D) according to the criterion of similarities and differences that can be seen in Figs. 6 and 7 (in respect of relationship nature and strength, i.e. whether value variation with current is strong or weak, not whether values as such are large or small). Name these groups, list all the devices (from among those investigated) that belong to either group and indicate specific similarities between them.
##### Group 1

##### Group 2

### Explain the above observations based on your knowledge about different current conduction mechanisms (unipolar / bipolar; Manual 0, Refs. I and J; Manual 1, Ref. A and D). Indicate devices where conductivity modulation of the lightly doped layer can be seen (specify how this manifests in the results under analysis).

### Based on Figs. 6 and 7 state whether the devices listed below differ from each other and if so, what this difference consists in and how large it is:
Only the parameters under analysis in this part of the report should be considered. Both values (large / small) and their variations with current (increasing / decreasing / constant; strong / weak) should be analysed. An answer may be either positive or negative.
#### the various bipolar transistors (list them);

#### * the single BJT and the Darlington BJT.

## Principal circuit static power loss
### Based on Tables 1 to 4, plot the principal circuit static power loss Ploss as a function of the principal current Io [all the three (* four) devices in a single plot]. To better visualise relationship nature and strength, create the plot both using the linear scale (for both axes) and the logarithmic one (for both axes).

(a)

(b)
Fig. 8. Principal circuit static power loss as a function of principal current: (a) linear scale; b) logarithmic scale
### Based on Fig. 8 compare the strengths of relationships observed for the particular transistors. For which transistor is this strength weaker and close to a linear one, and for which, stronger and what law is it close to?

### Relate the above observations to the results from point 2.2, referring to the algebraic formula relating power to voltage (quote this formula).

### How do the above observations relate to the division of devices into groups made in point 2.2?

### Based on Figs. 6 and 8 (not on any other data), assess the usefulness of each transistor as a switch (i.e. how beneficial its application is), according to the criterion of the on-state voltage and the principal circuit static power loss (not according to any other criteria). Consider the effect of the principal current, thus of the load that would be imposed by an application and therefore might be low in some circuits while high in others.

## Control power consumption
### Based on Tables 1 to 4, plot the average control power Pctrl as a function of the principal current Io, using the logarithmic scale for both axes [all the three (* four) devices in a single plot].

Fig. 9. Average control power as a function of principal current
### Indicate two groups (Manual 0, Ref. H) that the investigated devices can be divided into based on similarities and differences between them visible in Fig. 9, considering both control power values as such and their variations with current. Name these groups, list all the devices (from among those investigated) that belong to either group and indicate specific similarities between them.
##### Group 1

##### Group 2

### Explain the above observations based on your knowledge about the different control mechanisms (current / voltage and charge; Manual, Sub-Chapter 3.2; Manual 0, Ref. H; or in more detail: Ref. A; Manual 3P, Refs. A and B).

### Based on Fig. 9 state whether the devices listed below differ from each other and if so, what this difference consists in and how large it is:
The directive of point 2.4 should still be applied.
#### the various voltage and charge-controlled transistors (list them);

#### * the single BJT and the Darlington BJT.

## Static current gain
### Include source data and calculation results for the static forward current gain of the single (* and the Darlington) BJT in the saturation region [source data found in Table 1 (* and Table 2)] and in the quasi-saturation region [source data found in Fig. 2 (* and Fig. 3)
Table 5. Static forward current gain in the common emitter configuration for BJTs
Transistor	Operating Region	UCE / V	IC / ?	IB / ?	βF
Single	Saturation
	Quasi-Saturation	1
* Darlington	Saturation
	Quasi-Saturation	5

Formula used:
βF =
### Compare the calculated value of the static current gain in the quasi-saturation region to the value read out (indicate this value) from the static current gain characteristic included in the data sheet of the considered transistor for same values of collector current and collector-emitter voltage.
Assume that the measurement time was so short that the transistor’s temperature did not considerably increase above the room temperature.
#### for the single transistor;

#### * for the Darlington.

### Compare the static current gain value in the saturation region to its value in the quasi-saturation region.

### Based on the above observation, justify whether decreasing the principal circuit power loss—through bringing the transistor into its saturation region—requires the control power to be increased or, to the contrary, enables this power to be decreased.

### * Compare static current gain values obtained for the Darlington BJT to those obtained for the single BJT:
#### in the quasi-saturation region;

#### in the saturation region;

#### the ratio between the value in the quasi-saturation region and the one in the saturation region.

## BJT compared to other types of power transistors
### * Based on information and formulae given in Ref. B as well as on the results in Tables 1, 2 and 5, enumerate and explain all the differences between the single BJT and the Darlington BJT that have been observed in Parts 2 to 5.

### Referring to your answers given in Parts 2 to 4, formulate and justify ultimate conclusions concerning the value of each transistor in the role of a switch in various potential application circuits that impose different requirements, considering that an answer may depend on the principal current, thus on the load (which may be either heavy or light depending on the specific circuit):
#### primarily requiring a low control power consumption;

#### primarily requiring a low static power loss (in the transistor’s principal circuit);

#### requiring both a low control power and a low static power loss.

### Based on the results found in Parts 2 to 4 (and Part 5), point out arguments for applying BJTs in the role of switches in power electronic converters:
#### single devices;

#### * Darlingtons.