NN	5U	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Technical University of Lodz / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 5U / Two-Stage Cycloconverter / Manual version: 4.10 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Electronic ballast as a multi-stage power converter
### Insert the recorded oscilloscope images of voltages and currents in the ballast circuit.
For each oscilloscope image that contains more than one waveform, it is obligatory to describe each particular waveform (with its symbol), either directly in the image or in its caption (by referring to numerical designations appearing in the image or to colours provided the report will be delivered in colour).

(a)

(b)

(c)

(d)

(e)

(f)

(g)
Fig. 1. Voltage and current waveforms in the investigated ballast circuit: (a) ug; (b) urect, ug ; (c) ump, urect; (d) ump, ifl; (e) ump, −iC2, ifl; (f) ufl (wraz z uHZ i uFZ); (g) ump, ucap, uinv
### Include read-out and calculation results based on oscilloscope images of Fig. 1.
Table 1. Electrical quantity waveform parameters in key points of the investigated ballast
Parameter	ug	urect	uinv	ifl
Shape
Frequency
Alternating component magnitude
Direct component level
Alternating component presence
Direct component presence

### Based on the schematic and the description of the investigated circuit (Section 4.1 and Ref. C), create its block diagram (cf. Fig. 4 in Ref. B). Include designations of the physical quantities found in Table 1 according to the locations where they occur and mark the input and the output of the converter (as a whole).
Disregard the isolation transformer that was present in the experimental circuit since it was not part of the ballast, but just a safety device.

Fig. 2. Block diagram of the investigated ballast
### Based on Table 1:
#### point out parameters that are modified by this converter (considering the output of the converter as a whole with respect to its input; Manual 0, Ref. B), determine in which direction this occurs (increase / decrease) and calculate the rate of this change (the ratio of the value observed at the output to the respective value at the input or vice versa);

#### classify the investigated circuit in terms of the four basic power converter groups (Manual 0, Ref. F; refer to specific results in Table 1 and observations from point (a));

#### show that the investigated converter is a multi-stage one (Ref. C [22], Section 2.1; Manual 0, Ref. F, Section 1‑4‑2).

## Half-bridge inverter operation
### * Analyse the half-bridge capacitor voltage waveform ucap.
#### From appropriate oscilloscope images in Fig. 1 (both chosen images should have been recorded at the same time base), read out the direct component Ucap(0) of the ucap voltage as well as the direct component Urect(0) of the rectified voltage urect. Enter the values obtained into Table 2.
According to the Fourier’s theorem, the value of the direct component of a physical quantity equals the average value of this quantity (the Mean indication of the oscilloscope).
#### Do the form (shape) and the value of the capacitor voltage conform to theoretical predictions (Ref. C [22], Appendix 1; quote those predictions)?
When comparing numerical results, take measurement uncertainty into account as given in the manual.

Table 2. Parameters of electrical quantity waveforms in the innverter
Ucap(0)
Urect(0)
Ump(0)
Ump(a),m

### * Analyse the waveforms of the inverter’s output voltage uinv.
#### From the appropriate oscilloscope image in Fig. 1, read out the value of the direct component Ump(0) and the magnitude of the alternating component Ump(a),m of the halt-bridge arm middle point potential ump. Add the values obtained to Table 2.
#### Justify the form and both characteristic values of the inverter’s output voltage waveform (Table 1) based on this circuit’s topology, the Kirchhoff’s voltage law as well as on the observed forms of the ucap and ump voltages observed and on their values read out (Table 2; Ref. C [22], Appendix 1).
The remark in point 2.1(b) still applies.

#### How does the magnitude of a half-bridge inverter’s output voltage uinv relate to its constamt input voltage urect?

### By analysing appropriate oscilloscope images from Fig. 1 and referring to specific waveform features that can be seen therein, relate the waveform of the output current ifl to the one of the inverter’s output voltage uinv (Ref. C [18], “Operation Description”; [22], Appendix 1).

### Does the presence or lack of a direct component in the output current of the investigated inverter (which can be considered identical to the lamp current ifl to a good approximation) as indicated in Table 1 conform to theoretical predictions for the half-bridge topology (Ref. C [18], “Controlling the Fluorescent Lamp”; quote this prediction)?

### By analysing an appropriate oscilloscope image from Fig. 1 and referring to specific waveform features that can be seen therein, relate the waveform of the collector-emitter voltage of the transistor Q2, uCE2 (which equals the half-bridge arm middle point voltage ump) to the waveform of the inverter’s output voltage urect (Ref. C [22], Appendix 1).

### Based on an appropriate oscilloscope image from Fig. 1, referring to specific waveform features that can be seen therein:
#### relate the waveform of the collector current of the transistor Q2, iC2, to the waveforms of the inverter’s output current ifl and of the collector-emitter voltage uCE2 (Ref. C [18], “Half Bridge Topology Analysis”, “Half Bridge Design”; [22], Section 4.2.1);

#### justify the relationships observed by referring to the different states of this transistor Q2 considered as a switch, to its directionality (forward / reverse bias of its principal circuit, i.e. the direction of its collector current) as well as to the Kirchhoff’s current law.

## Transistor operation in the inverter
### From an appropriate oscilloscope image in Fig. 1, for the transistor Q2, read out the maximum working values of the collector-emitter voltage uCE2 and the collector current iC2 (keeping in mind that the latter was recorded after being inverted, i.e. as −iC2). Enter the results obtained into the table below.
Table 3. Maximum working values of operating point coordinates for the transistor Q2
UCE2(m)
IC2(m)

### Compare the above maximum working values to the rated (maximum admissible) voltage and current for the transistor used. Calculate the safety margins applied by the designer, expressing them as percentages of the respective rated values.
##### Voltage
In the case of the rated voltage, attention should be paid to selecting the right one of the two rated parameters (Manual 5P, Ref. A; Ref. C [18], “Breakdown Voltage”). Assume that one can take full advantage of the fact that base and emitter are not open in the investigated circuit.

##### Current

### In the diagram of the safe operating area of the transistor used included in its data sheet (* with the operating point trajectory superposed on it), localise and mark the extreme operating points of the transistor Q2 in its static states: its peak conducting current iC2(pk) and its peak blocking voltage uCE2(pk). Do these points (* as well as the entire trajectory) fit within the limits of the safe operating area?
The voltage drop in the conducting state or the leakage current in the blocking state are not known; they should be assumed to be negligible, thus equalling zero.

Fig. 3. Safe operating ara of the transistor Q2 with extreme static operating points marked (* and wit the operating point trajectory superposed) as measured in the investigated circuit
### Based on your results presented in Table 1 and in point 3.1, state how the required minimum ratings of the transistors relate to supply and load conditions (approximately equal or clearly lower or higher and by what approximate ratio) in the case of a half-bridge inverter:
#### voltage capability (peak working voltage), to the magnitude of the output voltage (uinv) and to the input voltage (urect);

#### current capability (peak working current) to the magnitude of the output current (ifl);

#### * current capability (rms working current) to the rms value of the output current (predict their mutual ratio by comparing appropriate waveforms of Fig. 1).

### Within the offers of semiconductor device retailers, find one, possibly the cheapest, transistor of either type: MOSFETand IGBT with rated parameters (voltage and current) close to the respective ratings of the BJT used in the investigated circuit. Collect the prices and the ratings of these transistor (including the BJT) in the table below. Insert corresponding web site fragment images.
Is is likely that some ratings will have to be greater than for the transistor used in the investigated circuit. However, they cannot be considerably lower as such a transistor would not be a suitable replacement. As a general rule, consider the criterion of a similar current capability in the first place, and an equal or greater voltage capability, in the second place.
All the prices should be expressed in the same currency, be all net or all gross prices, and apply to similar numbers of items.
Table 4. Prices for the BJT originally used in the investigated circuit and for transistors of other types with similar ratings
Transistor type	Designation	Urat / V	Irat / A	Price
BJT	BUJ100
MOSFET
IGBT

Fig. 4. Source data for Table 4
### Describe price relations between the above transistors. Do they justify the application of BJTs in power electronic circuits in spite of more recent devices with undoubted advantages (MOSFET, IGBT) being available?

## Interaction with the fluorescent lamp
### From appropriate oscilloscope images in Fig. 1, read out and enter into the table below: the rms value of the lamp current Ifl(rms), its maximum value Ifl(m) and the rms value of the lamp voltage Ufl(rms).
As the lamp current has no direct component, is maximum value equals half of its peak-to-peak value (Peak-Peak indication).
Table 5. Lamp operating parameters read out or calculated
Ifl(rms)
Ifl(m)
Ufl(rms)
kc(ifl)
Pfl
Rfl(eq)

### Based on the present data in Table 5, calculate and add to this table:
#### the crest factor of the lamp current kc(ifl), from its definition (manual, Section 5.1);
#### lamp average (electrical) power Pfl, from the Joule’s law assuming that a fluorescent lamp behaves as a resistive device after ignition;
#### equivalent lamp resistance Rfl(eq), obtained by applying the Ohm’s law to rms values.
### Based on appropriate results from Tables 1 and 5 as well as on lamp data given in the manual (Sub-chapter 4.1), assess whether the investigated circuit correctly fulfilled its role of a fluorescent lamp ballast in respect of:
#### operating frequency (Ref. B, “Increased light output”);

#### limiting lamp current to an optimum value (calculate this value; Ref. C [18], “Controlling the Fluorescent Lamp”);
The optimum value should be calculated using the rated power of the lamp used (as given in the manual) and its equivalent resistance (as calculated above). The rms voltage value measured cannot be directly used for this purpose as this value occurred just at the measured current which can be different from the optimum one; on the other hand, the equivalent resistance can be considered independent of current (in its limited range).
Ifl(rms),opt = ?

#### lamp current shape (as described by its crest factor; Ref. B, “The fluorescent lamp”) appropriate for maximising lamp life time.

## * Rectifier and electromagnetic compatibility
### Insert oscilloscope images of voltages and currents in the rectifier recorded for different filter capacitance values.
In the case of the output voltage for the initial capacitance, Fig. 1(b) just has to be copied.
The directive of point 1.1 still applies.

(a)

(b)
Fig. 5. Rectifier input voltage and current waveforms for two different filter capacitance values: (a) C4 = ?; (b) C4 = ?

(a)

(b)

Fig. 6. Rectifier output voltage waveforms for two different filter capacitance values: (a) C4 = ?; (b) C4 = ?
### Insert time-domain and frequency-domain comparative plots of the current drawn from the grid for different filter capacitance values.

(a)

(b)

Fig. 7. Current drawn from the grid for two different filter capacitance values: (a) time-domain waveform together with the grid voltage; (b) frequency spectrum
### In the table below, include values read out or calculated based on appropriate oscilloscope images from Figs. 5 and 6.
Table 6. Electrical quantity waveform parameters in the rectifier as read out or calculated for two different filter capacitance values
C4 / ?
Urect(pp) / ?
Urect(av) / ?
rurect
Pg / ?
Ug(rms) / ?
Ig(rms) / ?
Sg / ?
λ
fg(1) / ?
dh(ig)
φg1 / ?
λ′

### Based on the results from Table 6, determine how the change in the filter capacitance affected the various operating parameters of the rectifier.
#### In which direction did the ripple factor of the rectifier’s output voltage ruo change as a result of the increase in the filter capacitance?

#### In which direction did the total harmonic distortion of the current drawn from the grid dh(ig) change as a result of the increase in the filter capacitance?

#### Are the requirements of a small ripple magnitude at the rectifier’s output and the one of a low harmonic content at its output compatible or contradicting?

### Based on Fig. 7, determine what caused the increase of the total harmonic distortion of the current drawn from the grid after the filter capacitance was increased.
#### In what way did the waveform of the current drawn from the grid change as a result of the increase in the filter capacitance (refer to specific dimensions of a geometric figure)?

#### Did the shape of this current thus become more or less similar to a sine wave?
The above can only be visually assessed by comparing against the grid voltage waveform. However, only the shape should be analysed, not values, because current values cannot be compared to voltage ones.

#### How did the above translate into the values of the fundamental component and of harmonic components?

#### Justify the observation of point (c) referring to your conclusion from point (b).

#### Based on your observation from point (c) and referring to the definition of total harmonic distortion (Ref. E, Section 16.3.2; quote this definition), justify the change of this parameter observed in point 5.4.

### Verify the relationship between power factor and total harmonic distortion.
#### Based on the oscilloscope image of the grid voltage ug of Fig. 5 determine whether conditions occur under which the analytical relationship between power factor and total harmonic distortion holds (Ref. E, Section 16.3.2). Quote this condition (contained in the section heading) and this relationship (derive one formula based on appropriate two equations).

#### Based on appropriate results from Table 6, check whether the above relationship truly holds for the investigated circuit. Add power factor values calculated in the process to the result table as λ′.

### Using the values of average output (lamp) power Pfl and of average input power (drawn from the grid) Pg from Tables 5 and 6, calculate the efficiency of the investigated cycloconverter.
η = ?