NN	6P	1
Team	Exercise	Revision *

Date of receipt **

Result of evaluation **

Lodz University of Technology / Department of Microelectronics and Computer Science

Laboratory report / for / Power Devices and Systems

Exercise 6P / Power Loss under Switched-Mode Operation / Manual version: 7.2 Report template version: 0

Laboratory session date(s)
Team composition during laboratory session

* To be incremented for each subsequent revised document delivered.
** Filled in by the teacher.

In case this document is to be edited using Microsoft Word, it should first be saved in the doc format (or docx provided the newest software care used) from LibreOffice Writer and only then, opened in Word. Otherwise, formatting, elements generated automatically and internal links will become corrupted.
Remarks on exercise realisation

Symbols

## Circuit components
### From Schematic, paste the definitive schematic diagram of the circuit simulated.

Fig. 1. Schematic diagram of the low-side switch circuit simulated
### Provide parameter values for the control source ug.
Table 1. Control source parameters
Parameter	Value	Unit
PER
TP
TD
TR
TF
V1
V2

## Comparison of energy dissipation and power loss components
### Insert voltage, current, power and energy waveforms obtained of two (* three) switching frequencies, for a full switching period and for either dynamic state. All the plots that concern a given frequency should be located on the same (single) page.
For all the simulation results, the different waveforms should be clearly described in figure labels or directly in the images (by referring to e.g. symbols, colours or letter designations as used by Probe). If waveform layout remains identical in subsequent plots, it will be sufficient to make reference to Fig. 2.

(a)

(b)

(c)
Fig. 2. Circuit waveforms for switching frequency fs,ini = ? (control voltage ug, uGS, iD, uDS, drain power loss pD, energy dissipation WD): (a) full switching cycle; (b) turn-on state; (c) turn-off state

(a)

(b)

(c)

Fig. 3. Circuit waveforms for switching frequency fs = ?: (a) full switching cycle; (b) turn-on state; (c) turn-off state

(a)

(b)

(c)

* Fig. 4. Circuit waveforms for switching frequency fs = ?: (a) full switching cycle; (b) turn-on state; (c) turn-off state
### Include numerical results obtained through simulations and calculations, in an increasing order of switching frequencies.
To make analysis easier and to ensure consistency in graphs, all the energy values and all the power values must be expressed in same units.
Table 2. Simulation and calculation results
fs / ?	×			*
Ts / ?	×
pD(pk) / ?	Turn-on
	Conducting
	Turn-off
	Blocking
WD / ?	Turn-on
	Conducting
	Turn-off
	Blocking
WD(tot) / ?	×
PD,stat / ?	×
PD,dyn / ?	×
PD / ?	×

### Based on your results in Table 2 for the initial switching frequency fs,ini, analyse the relationship between the instantaneous power loss and the energy dissipation in a transistor:
#### in which of the four operating states did the instantaneous power loss reach its highest peak value pD(pk)?

#### in which of the four operating states was the largest amount of energy WD dissipated?

#### did the highest instantaneous power loss and the greatest energy dissipation occur in the same state or in different states of the transistor?

### Explain the above observations based on the formula relating energy to power (Ref. A); in this context, you may optionally refer to the instantaneous power pD waveform of Fig. 2.

### Based on your results in Table 2 for the initial switching frequency fs,ini, compare:
#### the instantaneous values of power loss in static states (represented by the appropriate values of pD(pk)) to the static average power loss PD,stat;

#### the instantaneous values of power loss in dynamic states (represented by the appropriate values of pD(pk)) to the dynamic average power loss PD,dyn.

### Explain the differences observed based on the average power definition (Manual 0, Ref. C or G) and derived formulae (Ref. A).

### * Based on Table 2, justify whether the results obtained legitimise the assumption that the influence of the blocking state on static average power loss is negligible.

### * Check whether the expected relationship holds between the static average power loss and the on-state instantaneous power loss (Ref. A; the static term has to be extracted from the total average power formula). Quote this relationship and calculations made.

## Effect of switching frequency on energy dissipation
### Based on results in Table 2, determine which of the four components of energy dissipation in the transistor remain constant and which ones change with switching frequency increasing. What way do the latter vary in?
Due to the uncertainty of value read-out from plots, resulting from some of the dynamic state boundaries being vague, any difference of less than 10% should be considered no change.

### Based on Figs. 2 and 3 (* 2 to 4), determine:
#### which operating states’ duration results from the control waveform frequency and which, from the transistor’s properties;

#### whether the instantaneous power waveform within each particular operating state changes with switching frequency; if it does, then in what way?

### Explain your observations from point 3.1 based on the relationship between power and energy (point 2.4), referring to your answer from point 3.2.

### Based on Table 2, create a plot showing the energy dissipated in the transistor in its four particular operating states as a function of the switching frequency, in the form of a percent cumulative bar graph (a single one including all the frequencies for which results are available in Table 2).
A cumulative bar graph is intended for visual presentation of quantities composed of several components. (Note that in office packages the term bar graph usually refers exclusively to graphs oriented horizontally, while the traditional, vertically oriented graph may be called column graph instead.) In such a graph, bars corresponding to the particular components are not placed side by side, but are stacked one on another. Such a presentation form makes it easier to determine how important the contribution of each component is. At the same time, the total height of the bar corresponds to the total value of the given physical quantity equal to the sum of all its components.
A variant of the cumulative bar graph is the percent cumulative graph (called 100% stacked column in Microsoft Office and column percent stack in LibreOffice). Such a graph does not present absolute values as such. Each full (composite) bar therein has the same height labelled as 100%, with the meaning of 100% of a total value, while the heights of its particular component bars correspond to the percentages they constitute of this total value.
In accordance with reality, the Y-axis should be labelled as the ratio of energy dissipation in a particular state to the total energy dissipation over a switching period, i.e. WD/WD(tot).

Fig. 5. Contributions of particular operating states to the transistor’s energy dissipation over a switching period, as functions of switching frequency
### Based on Fig. 5, determine how the contributions of the particular operating states to the energy dissipation over a full switching period vary with switching frequency increasing.

### Justify the above observations based on your answer from point 3.1.

## Effect of switching frequency on power loss
### Based on Table 2, create a plot of the average power loss in the transistor, showing the shares of its static and dynamic components. The image has to be a cumulative bar graph (but not a percent one) where the bottom component bar corresponds to the static loss, while the top one, to the dynamic loss.

Fig. 6. Static and dynamic average power loss as a function of switching frequency
### Based on Fig. 6, determine if and how either component of the average power loss as well as its total value vary with switching frequency increasing.

### Based on suitable formulae (Ref. A or B) and referring to your results from points 3.1 to 3.3, explain:
#### why the static average power loss remains constant despite the energy dissipation in the static operating states varying with switching frequency;

#### why the dynamic average power loss varies with switching frequency despite the energy dissipation in the dynamic operating states remaining constant.

### * Plot the dynamic average power loss PD,dyn as a function of the switching frequency fs.

Fig. 7. Dynamic average power loss as a function of switching frequency
### * What is the nature of the relationship plotted? Does it conform with what the theory predicts (Ref. A or B; quote a suitable formula, appropriately transformed if necessary)?

### Referring to facts and relationships visible in Figs. 5 and 6, justify which criterion should be applied for transistor selection with the aim of minimising the power loss: one of small conduction (static) power loss or one of small switching (dynamic) power loss? Consider each of the following two cases separately:
#### low switching frequency;

#### high switching frequency.